## Slide 1: Ray Tracing in Entertainment Industry
Tanaboon Tongbuasirilai
Dept. Computer Science
Kasetsart University
Week 10

## Slide 2: Simple visual effects
Depth of Field (DoF)
Motion blur
Notes: Dof  found in many film / movie / game productions
Related to human eyes
Motion blur  giving clues of moving objects

## Slide 3: Depth of Field (DoF)
Depth of field is the effect in which objects within some range of distances in a scene appear in focus, and objects nearer or farther than this range appear out of focus.
Depth of field is frequently used in photography and cinematography to direct the viewer's attention within the scene, and to give a better sense of depth within a scene.
https://developer.nvidia.com/gpugems/gpugems/part-iv-image-processing/chapter-23-depth-field-survey-techniques
Notes: definition

## Slide 4: Thin Lens
https://developer.nvidia.com/gpugems/gpugems/part-iv-image-processing/chapter-23-depth-field-survey-techniques
Notes: Many parameters involve to focus.
This image is a typical focus scenario =
Sharp projection (projection in the focus) is at V
The equation shows sharp focus.

## Slide 5: Circle of Confusion
When the CoC is smaller than the size of a pixel, that pixel is in focus while a CoC larger than a pixel will be out of focus and cause blurring
Sharp focus line is depicted by green dashed lines.
Notes: What if the object is moved out of the focus.
Image plane = where sensor lies
Focus scenario = dashed lines
DOF scenario = green lines
Class discussion
What parameters affect to circle of confusion ?
A – aperture  affect to DOF ?

## Slide 6: A tricky camera model
So far, we simulate this kind of pinhole camera model.
Center of the camera.
Notes: We put a camera at the pinhole.
Aperture = camera

## Slide 7: Adding Lens to the pinhole
Notes: Now add lens to the pinhole = aperture added = circle of confusion created

## Slide 8: Comparison
https://steveharveynz.wordpress.com/2012/12/21/ray-tracer-part-5-depth-of-field/
- Lens has its radius.
- Do sampling inside lens radius.
- Take the average of sampled rays.
Do sampling at the center of the lens.

## Slide 9: Lens radius can be found by using Focus distance and Defocus angle.
Radius
- Virtual film
- Focus plane
Focus distance
Defocus angle
Notes: 2 parameters can be used to infer another one.

## Slide 10: Add DoF in our code
Notes: (old) Ray origin = camera origin
(new) Ray origin = random inside a virtual lens (DoF applied)

## Slide 11: Motion Blur
“Motion blur is an effect that manifests as a visible streak generated by the movement of an object in front of a recording device. It is the result of combining apparent motion in the scene and an imaging media that integrates light during a finite exposure time. This relative motion can be produced from object movement and camera movement and can be observed both in still pictures and image sequences. In general, sequences containing a moderate amount of motion blur are perceived as natural, whereas its total absence produces jerky and strobing movement”
https://graphics.unizar.es/papers/Navarro_motionblur.pdf
Notes: definition

## Slide 12: Origin of the phenomenon
Time is one of the most important parameters.
Radiance
Relevant parameters such as optics, shutter, aperture and film.
When taking a picture, scene radiance is captured by a camera. Additionally, intrinsic parameters of the capturing device influence to natural effects such as motion blur.
Radiance information of an image
Notes: Taking a picture = capturing radiance + intrinsic parameters of the capturing device
Integrating over time domain if radiance changed over time or other parameters changed.

## Slide 13: Formalized equation
Geometric term (Occlusion term, Visibility term)
Spatial term
Temporal term
Spatio-temporal relationship

## Slide 14: Time interval
Time Interval Ray Tracing for Motion Blur (TVCG 2017) (youtube.com)

## Slide 15: A simplified Space-Time ray tracing for motion blur
An object is allowed to be moved.
A ray has a time parameter.
Key idea : A random time sample captures a moving object independently.
Notes: Explain a bit about motion blur
Moving object -> space parameter(according to time)
Time -> time parameter

## Slide 16: Updating Ray class

## Slide 17: Updating an object class
Notes: Enough ?

## Slide 18: Updating scattering behavior !
A material class
The camera class

## Slide 19: Codes and class assignment !
Github : RT-python-week10
  https://github.com/KUGA-01418283-Raytracing/RT-python-week10